## Slide 1
TI FTRC
Advanced Algorithms for THz Sensing and Recognition
Murat Torlak and Yiorgos Makris
University of Texas at Dallas
2019 Annual Review

## Slide 2
Static Hand Gesture Recognition
Data Collection and Processing

## Slide 3: Static Hand Gestures
Fist
Two
Palm
C
Perpendicular (perp)
Thumbs Up (tu)

## Slide 4: NEW Static Experiment Parameters
Using TI mmWave radar equipment is set up specifically for hand gesture data collection.
Samples are taken of each hand static gesture from a distance of 0.35m to 0.55m from the radar with a constant, distant background.
Six gestures are used in addition to a ‘none’ gesture (without any hand in the specified range)
Radar Parameters:
  3 TX, 4 RX (12 Virtual MIMO Channels)
  16bit, Complex1x
  Start Frequency: 77GHz New Maximum Range:
  Bandwidth: 3.99948GHz Rmax = 3m
  Slope: 99.987 Hz/s
  ADC Samples: 64
  Sample Rate: 2000 ksps

## Slide 5: New Setup
Horizontal orientation
25 hand locations
35-55cm range
  Increments of 5cm
  Azimuth angles of 7°
  and 14° on either side
Little to no variation
vertically

## Slide 6: New Setup
As shown below, capture FOV ranges from 35-55cm
across a FOV of
28°, at increments
of 5cm.
Multiple AoA
14°
7°
7°
14°
35cm
5cm
55cm

## Slide 7: Data Collection

## Slide 8: Degrees of Freedom
30° of rotation in each direction
  Side to side
  Forward and backward
  Left and right
Different hands used (different reflectivity etc.)
30°
30°

## Slide 9: Degrees of Freedom
30°
30°
30°
30°

## Slide 10: New Raw Range Data

## Slide 11: New Raw Range Data

## Slide 12: Calibration
Phase offset due to spatial differences in multiple Tx and Rx antennas
Find out phase difference between channels due to this with
Correct the offset for each channel by comparing simulated and measured IF signal for each channel
Coefficients generated for 8 channels ()
Coefficients to be generated and used for 12 channels ()
C1
C2
C3
Cn
…
: Phase difference between
antennas
: Antenna Spacing in virtual array
: Angle of arrival
: Wavelength

## Slide 13: Preprocessing Techniques
Optimize Range FFT size
  Find optimal number of features from which machine learning algorithm can distinguish
Normalized to zero mean and unit variance
Dataset 1: Small dataset with 600 captures, no range or angle variation, high resolution (3Tx – 12 Channels): 95.45%
Dataset 2: Large dataset with 24,000 captures, increased variation, high resolution (3Tx – 12 Channels): 51.85%
  When gesture is close to the body, a shadow from the body buries the gesture
  Introduction of many variables (range/angle) stretches the limits of our current preprocessing techniques
Control/Minimal Preprocessing

## Slide 14: Range FFT Format
Range FFT produces a 12 x n array with 12 virtual channels and n range bins
...
...
...
Channel 1
Channel 2
Channel 3
Channel 4
Channel 5
Channel 6
Channel 7
Channel 8
Channel 9
Channel 10
Channel 11
Channel 12
R1 | R2
Rn

## Slide 16: Reformatting Range FFT
...
Channel 1
Channel 2
Channel 3
Channel 4
Channel 9
Channel 10
Channel 11
Channel 12
R1 | R2
Rn
...
Zero Pad
Zero Pad
Channel 5
Channel 6
Channel 7
Channel 8
Zero Pad
Zero Pad
Reformatted Range FFT to align with virtual array produces array of size 8 x n x 2
Accuracy: 97.98%
Notes: Make slide about real/complex layering of machine learning network

## Slide 17: 2D Range-Angle FFT
After Range-FFT, another FFT is performed across the sensor dimension to produce the Range-Angle FFT.
The angle domain shows a peak at the azimuth angle of arrival for returning chirp signals.
We will consider a region of the Angle-Range FFT in which we expect the gesture to appear.
...
R1 | R2
...
Dimension 1
Dimension 2
Accuracy: 95.96%

## Slide 18: Network Complex Layering
Input layer to the convolutional neural network
With Range FFT data, input image is of size n x 12 x 2
Current constraints limit the dimensions of the input layer for the Range-Angle FFT to n x 8 x 4
n = number of range bins
...
R1 | R2
...
Real Part
Imaginary Part

## Slide 19: Range-Angle FFT Peak Alignment
Dimension 1
Dimension 2
Notes: We locate the peak in the region which we expect to contain the gesture, then we select a window surrounding that peak

## Slide 20: 2D Autocorrelation
2D Autocorrelation
  Common peak location among all instances
  Resolves spatial differences from gesture types
  Possibly infeasible moving forward
Accuracy: 84.85%

## Slide 21: Conclusion
Progress towards high accuracy systems
Developing synergy between data collection, preprocessing, and machine learning
Data Collection
  Start with constant range
  Each dataset includes more variation
Time-Frequency Analysis (STFT)
Future Work