## Slide 1: The Radar Musical Instrument
Josiah W. Smith

## Slide 2: Hello!
Josiah Smith
BS Electrical Engineering – UT Dallas
  Radar + machine learning research
  2x senior capstone 1st place (team leader)
  3 years start to finish
PhD Electrical Engineering – UT Dallas
  Signal processing + hybrid algorithms
  Radar imaging, tracking, localization
  3 years start to finish
Industry Experience
  Texas Instruments Research
  IMEC Research
  Apple
Ecuador with my wife Morgan

## Slide 3: Radar Musical Instrument – Outline
Radar Signal Model for Musical Control
  MIMO-FMCW mmWave Radar
Conventional Feature Extraction
  Range, Cross-range, Doppler Signatures
  Mapping Spatial and Temporal Features to Music
Enhanced Feature Extraction & Tracking
  Image-to-Image Super-Resolution Neural Processor
  Doppler-Corroborated Particle Filter

## Slide 4: Introduction / Motivation
Low-cost millimeter-wave (mmWave) radar has a host of applications from commercial sensing, security screening, medical imaging, and human-computer interaction
Problem Statement: leverage the richness of the mmWave return signal to create an efficient, high spatial-resolution framework for precise human-computer interaction and digital instrument control.
Prior work:
  Camera, RGB+D camera, camera + radar systems, Theremin
  Issues: spatial resolution, privacy

## Slide 5: Frequency-Modulated-Continuous-Wave Radar
Receive time-delayed version of Tx signal
Tx Chirp
Rx Chirp
f
t
Tx Chirp
f
t
IF Signal
f
t
IF Signal
f
t
Fourier Transform
Transmit linear FM chirp
Demodulate to obtain IF signal
Target
Frequency contains spatial information

## Slide 6: Doppler Radar
Doppler Effect
  FFT across multiple FMCW pulses
Sensing distance: < 1 m
Goal: 3-D x-y-z localization
Issue: efficient MIMO near-field image reconstruction
Range-Doppler is not enough

## Slide 7: Multistatic-to-Monostatic Compensation
2
MIMO Array
Virtual Array
Round-trip distance
For small distances between Tx/Rx pairs
Multistatic Data
Monostatic Data
Compensation Procedure

## Slide 8: Efficient Near-Field Spatial Imaging
Near-field spherical wavefront
Received signal
Naïve approach (matched filter beamformer)
z
y
Tx/Rx
Target

## Slide 9: Efficient Near-Field Spatial Imaging
Near-field spherical wavefront
Received signal
Efficient approach – key step
z
y
Tx/Rx
Target

## Slide 10: Efficient Near-Field Spatial Imaging
Near-field spherical wavefront
Received signal
Efficient approach (Range Migration Algorithm – RMA)
z
y
Tx/Rx
Target

## Slide 11: Tangent – Efficient Freehand Imaging
Traditional Array Imaging
Emerging Imaging Applications – Arbitrary Scanning Geometry
BPA – 3 hr
RMA – 1 s
Ours – 1 s

## Slide 12: Conventional Feature Extraction
Maximum likelihood estimator of range (), cross-range (), and Doppler ()
RMA
1 m/s

## Slide 13: Music Theory for Engineers
Notes and Pitch
  Pitch = fundamental frequency
  Single frequency sinusoid with natural acoustic harmonics
Frets
  Quantize finger placement on some stringed instruments
Vibrato
  Frequency modulation applied to pitch
Thanks to listening-singing-teacher.com

## Slide 14: Mapping Radar Signatures to Music
Range  note selection
  Vertical position to select desired note
  Virtual fret quantize range into regions
Cross-range oscillation  vibrato
Doppler  MIDI parameter

## Slide 15: Simple Methods

## Slide 16: Enhanced Feature Extraction
Enhance RMA images with neural processor prior to feature extraction
Feed extracted-enhanced features to computer vision tracking algorithm
Raw Images
Neural Processor
Enhanced
Computer Vision Tracking Algorithm

## Slide 17: Spatial Super-Resolution
Image super-resolution emerging in ML / DL arena
Image upscaling akin to spatial super-resolution
Non-linear approach to leverage context / prior on images and signals
Can hybrid methods employ signal theory + ML for spatial and frequency super-resolution?

## Slide 18: Tangent – Frequency Super-Resolution
Frequency super-resolution signal extrapolation
Proposed Solution: hybrid algorithms (signal processing + ML)

## Slide 19: Tangent – Frequency Super-Resolution
4 GHz bandwidth  3.75 cm resolution
8 GHz bandwidth  1.875 cm resolution
Two scatterers separated by 2 cm
Raw 4 GHz Data
4 GHz  8 GHz Bandwidth Extrapolation
Artificially / blindly improve spectral  spatial resolution

## Slide 20: Spatial Super-Resolution FCNN
Image-to-image enhancement
  Remove distortion, blur, noise, clutter, etc.
  Improve subsequent feature extraction
Train on real data from human hands + synthetic simulated data

## Slide 21: Particle Filter Tracking
Particle filter (condensation algorithm) tracking
  Computer vision approach
  Can handle sudden movements and non-linear dynamics
Leverage Doppler for dynamic particle drift weighting
Dynamically update “importance” weight of new measurement

## Slide 22: Enhanced Methods

## Slide 23: Results – Ground Truth + Simple Methods

## Slide 24: Results – Particle Filter + Doppler
FCNN Improves Doppler SNR

## Slide 25: Results – Ground Truth + Simple Methods

## Slide 26: Hardware & Software Implementation
Hardware Setup
  TI 77 GHz mmWave MIMO-FMCW Radar
  TI High Speed Data Capture Card
Software Implementation
  MATLAB Interface
  Custom C++/MEX software stream data from TI radar to MATLAB in real-time

## Slide 27: Results – Simple Methods
Content available on IEEE Xplore

## Slide 28: Results – Enhanced Methods
Content available on IEEE Xplore

## Slide 29: Conclusions
Radar Musical Instrument
  Signal processing + machine learning + computer vision = hybrid-algorithms
  High-fidelity tracking framework without any optical sensor
  Surpass theoretical spatial resolution limitations
Why APL?
  Intersection of research and defense industry
  Impactful work on critical challenges
  Rapid learner & contributor
  Solving new problems and “owning the problem”

## Slide 30: Music Demo
Content available on IEEE Xplore