## Slide 1
Advanced Algorithms for Terahertz Sensing and Recognition
Murat Torlak and Yiorgos Makris
University of Texas at Dallas
Texas Instruments Foundational Technology Research Program on Millimeter Wave and High Frequency Microsystems
University of Texas at Dallas
June 12, 2020

## Slide 2: Advanced Algorithms for THz Sensing and Recognition
Description: Understand the limitations and challenges in THz FPA/IR imaging technology; identify solutions for target applications such as 3D gesture recognition, movement and presence detection.
Goals: Develop advanced real-time multi-antenna signal processing techniques for THz FPA/IR sensors to reconstruct and recognize targets in complex environments.
Principal Investigators: Murat Torlak (University of Texas at Dallas)
Yiorgos Makris (University of Texas at Dallas)
Students Current Status
Josiah W. Smith (MT) PhD (Fall’19)
Shiva Shankar Thiagarajan (YM) PhD (Sp’18)
Bhaskar Raj Upadhyay (MT) PhD (Fall’18)
Richard Willis, (YM) Intern
TI Liaisons:
Aleksandar Purkovic, Arthur Redfern, Anand Dabak, Dan Wang

## Slide 3: Plans and Deliverables (Year 2/3)
Milestones
  Developed a MATLAB based GUI to streamline raw mmWave radar and IR sensor data collection
  Performed the initial testing of machine learning methods with real mmWave data sets
  Two PhD students (Josiah/Bhaskar) working on various application such as gesture recognition/imaging with 77GHz TI radar until THz radar becomes available
  Students (Richard/Shiva) working on advances machine learning algorithms for dynamic gestures (static gestures before), implemented a flexible python-based infrastructure for gesture recognition using radar information.
  Trained models were investigated for various shortcomings and refined to improve the model robustness.
Deliverables
  Software on the HGR DSP and ML methods (Nov. 15, 2020)
  THz imaging testbed (Nov. 15, 2020)

## Slide 4: Revised Schedule after TI Feedback
Year | 1 | 2 | 3 | 4 | 5
Milestones | Develop a detailed mathematical model for THz FPA with reflectors and THz transceivers. Develop a geometric reference model including Doppler shift patterns for 3D gesture recognition and motion detection Software implementation of machine learning algorithms for THz sensing/imaging. | Complete 24/77 GHz hardware demonstrator with existing chipsets to achieve millimeter-scale accuracy in 3D gesture recognition and motion recognition. Develop multi antenna signal processing to reduce speckles and to correct reflector aberration and machine learning techniques. | Software implementation of real-time multi antenna signal processing techniques and machine learning algorithms for THz-FPA on a custom CPU+GPU. Refine the mathematical models of THz-FPA and geometric models based on 77 GHz demonstrator results. | Verify and fine tune low complexity algorithms with THz FPA on silicon with TI and center collaborators. Software implementation of machine learning algorithms on a custom CPU+GPU for THz sensors. Finalize the algorithms to eliminate errors due to multipath. | (If all the milestones are met and authorized by TI) Build and characterize optimized resolution limits of THz FPA with THz chipsets incorporating reflectors and machine learning on CPU/GPU/FPGA for 3D gesture and motion recognition. Characterize the performance limits of aberration mitigation algorithms.
Deliverables | Report on the mathematical model of THz FPA with reflectors and THz radios Report on geometric models for 3D gesture recognition and the machine learning algorithms for THz sensing/imaging | Report on measurement results using 24/77 GHz demonstrator. Software implementation of multi antenna signal processing and machine learning for THz-FPA gesture and motion detection | Report on software implementation and refined mathematical models of the end-to-end sensing and imaging system with machine learning algorithms. Report on the algorithms to increase field of view. | Report on measurement results on the performance limits of multiantenna signal processing algorithms and machine learning techniques used in THz-FPA sensors. | Report on measurement results of fully functional THz-FPA imager enabled by real-time multiantenna signal processing algorithms and machine learning. CPU/GPU/FPGA software.

## Slide 5: TI Feedback
Well-attended monthly conference calls. Continuous engagement with TI engineers.
Preprocessing versus ML complexity for more efficient and lower error rate classification
  Response: Some pre-processing methods are very useful. Angle/Range FFT. More details will be given in the presentation.
How to quantify the preprocessing versus ML trade off.
  Response: Empirical complexity and accuracy analysis has been done for gesture recognition. More details in the presentation.
Hardware/software interaction
  Response: All of our processing is offline. We have been using our own MATLAB based GUI while mmWave radar studio is running in the background. For real-time operation, we have to port the algorithms into built-in DSP.
Pick an end application to target the system.
  Response: Gesture recognition has many elements to demonstrate the system performance. We are also looking at (narrowband) imaging as well.

## Slide 6
Front-End Signal Processing and Applications
Josiah W. Smith and Murat Torlak

## Slide 7: Outline
Static Pattern Recognition
Static Gesture Recognition
Sterile Gesture Training
Dynamic Pattern Recognition
Dynamic Gesture Recognition
Medication Packaging Insert Detection
Conclusion
Future Work
THz IC

## Slide 8: Static Gesture Recognition

## Slide 9: Old Setup
Move hand to multiple locations
Time-consuming process
75% classification accuracy

## Slide 10: New Static Data Collection – Scanner
Move radar along planar aperture
Quickly obtain many perspectives of gesture!

## Slide 11: Sterile Gesture Training

## Slide 12: Sterile Dataset
Human Hand– 40000/class
  3 gesture classes
Foil Cutout– 40000/class
  3 corresponding foil “cutout” classes
Size per class: (64, 8, 40000)
  64: range FFT bins
  8: virtual antennas
  40000: hand in different positions
Foil cutout has much higher RCS

## Slide 13: Sterile Gesture Training: Results
Scenarios:
Train with human data, test with human data
Train with 40% human data 60% cutout “sterile” data, test with human data
Range FFT Range Angle FFT
Results: 85% 90%
Results: 93% 95%
Conclusion: “sterile” data improves classification accuracy

## Slide 14: Sterile Gesture Training: Range FFT
Human + Sterile Data: 93%
Human Data Only: 85%

## Slide 15: Sterile Gesture Training: Range Angle FFT
Human Data Only: 90%
Human + Sterile Data: 95%

## Slide 16: Dynamic Gesture Recognition

## Slide 17: Dynamic Datasets
Dataset 5 – 600/class
  Horizontal antenna array
  Captured across different days, same subject
Dataset 6 – 1200/class
  Vertical antenna array
  Captured across different days, different subjects
Size of data for each class (64, 8, 64, C)
  64: range FFT bins
  8: virtual antennas
  64: slow-time (frame index)
  C: captures/class
Horizontal Array
Vertical Array

## Slide 18: Results
Preprocessing:
Range FFT -> use only hand and torso bins
Doppler FFT
Use only one sensor
Dataset 5 – Horizontal
  100% classification accuracy
Dataset 6 – Vertical
  98% classification accuracy
Combined – Horizontal and Vertical Data
  70% classification accuracy – can we improve??
Size of data for each class (25, 64, C)
25: range bins
64: doppler bins (velocity)
C: captures/class

## Slide 19: Computational Efficiency Analysis
Range FFT 40ms
Range FFT 1 Channel 40ms
Range Doppler
Range FFT
Range Doppler 1 Channel
Range, Angle, Doppler, 40ms
Range Doppler Filtered 1 Channel
BEST!

## Slide 20: Medication Packaging Insert Detection

## Slide 21: Medication Packaging Insert Detection
Problem Setup:
Box with bottle mounted on rotator
Radar scanned horizontally at constant speed
Discrete captures every 0.5mm
After each horizontal scan, rotation by 3.6°

## Slide 22: Binary Detection
Box contains either:
Pills in bottle and insert
Pills in bottle and no insert

## Slide 23: Conveyor Belt Scenario
Box moves along linear path
Orientation could be at any angle
Insert could face towards or away from radar
1000 samples/class
81% classification accuracy

## Slide 24: Rotator Scenario
Box is rotated in front of radar
Radar views all sides of the box
Multiple horizontal positions
4000 samples/class
99.9% classification accuracy

## Slide 25: Static Captures
Still images of box are captured
Box at multiple horizontal locations and orientations
More data points
400000 samples/class
82% classification accuracy

## Slide 26: Future Work: THz Imaging

## Slide 27: THz Imaging
THz IC – 0.41 THz
  Narrowband (~200MHz)
  2-D image capable
  In progress
TI mmWave Radar – 77GHz
  4GHz bandwidth: 2-D and 3-D image capable
  Use limited bandwidth to emulate THz chip
Use TI radar to verify narrowband imaging approach

## Slide 28: THz Imaging
TI Radar – Narrowband
Single frequency to mimic narrowband THz IC
High resolution 2-D image
TI Radar - UWB
Using 4GHz bandwidth
High resolution 3-D image
Single Frequency
500 MHz
200 MHz

## Slide 29: Conclusions and Future Work
Static Pattern Recognition:
Use scanner for fast data acquisition
Train using “sterile” data
Dynamic Pattern Recognition:
Doppler information is key for hand gestures
Ongoing and Future Work:
New applications: automotive & medical arenas
Continued synergy among TxACE groups to obtain THz IC

## Slide 30
Machine Learning Algorithms
Richard Willis
Shiva Shankar Thiagarajan
Yiorgos Makris

## Slide 31: Overview
Introduction
  Objective
  Dataset Definition
  Data Formats
Architecture and modifications
Results
Analysis for overfitting
Future Work

## Slide 32: Introduction
Objective – Develop machine learning models for recognizing dynamic gestures
Dynamic Gestures:
  Push
  Pull
  Circle
  Wave
  Whoosh
Range (m)
Frequency Response

## Slide 33: Introduction - Data
No. | Type | Total Captures | Gestures | Captures/Gesture | FFT Size | Frames | Tx/Rx Chs | 
1 | S | 12000 | 6 | 2000 | 256 | 1 | 4 | Original static
2 | S | 24000 | 6 | 4000 | 512 | 1 | 12 | Large Set
3 | S | 1800 | 6 | 300 | 64 | 1 | 12 | Low variation
4 | D | 2400 | 5 | 600 | 64 | 256 | 12 | Original dynamic
5 | D | 1000 | 2 | 600 | 64 | 512 | 12 | Larger dynamic set
Type: S=Static, D=Dynamic
All datasets utilize 4 receiver channels
Dynamic data set frame captures are ~5ms apart
Currently working on Dynamic Dataset 4.

## Slide 34: Introduction – New Data Format
New way of processing dataset 4
600 instances/gesture of [2, 25, 64]
  2 * 25 * 64 = 3200 features/sample
Previously, 600 instances/gesture of [2, 12, 64, 256]
  2 * 12 * 64 * 256 = 393,216 features/sample
~100x size reduction
  Faster loading, processing, training
  Reduced overfitting
Total size ~800Mb

## Slide 35: Architecture
1x4x4 Convolution
Stride = 3,4,4
16 channels out
2x4x4 Convolution
Stride = 3,4,4
16 channels out
LSTM:
3 Layers
Hidden State Size: 528
Fully Connected Layer
In:
2 x 25 x 64
Classifier Model
Out:1x5
3 x 24 x 61
Intermediate Dimensions
9 x 23 x 60
1x12,420

## Slide 36: Hyperparameter Tuning
Using Facebook’s Ax platform
Similar graphs generated (not shown) for other hyperparameters
High accuracy, low standard error from cross validation
Low accuracy, learning rate/momentum too high

## Slide 37: Cross Validation
Repeat training using different parts of dataset for validation each time
Helpful to prevent overfitting to a part of the dataset
https://en.wikipedia.org/wiki/Cross-validation_(statistics)

## Slide 38: Results
Using Ax to tune hyperparameters, 5 cross-validation runs:
  Train Accuracy Avg: 94.8%, Std: 2.1%
  Validation Accuracy Avg: 95.2%, Std: 2.6%
  Test Accuracy Avg: 93.5%, Std: 2.7%
There was a slight decrease from the ideal accuracies observed with the previous data format
  Complexity/accuracy trade-off
  Substantially faster, smaller network

## Slide 39: Analysis for Overfitting
Low Shot learning is learning based on a single or small number of training instances
Imprinting is a type of low shot learning
(see right)
Imprinting method can serve as a tool to quantify the overfitting in the network
Worked as expected – not perfect, but relatively high accuracies in most cases with a few low outliers
Allows for making improvements to the model and validating its robustness.
Ref: Low-shot Learning with Imprinted Weights (https://arxiv.org/abs/1712.07136)
Thanks to Arthur Redfern (Liaison) for his feedback

## Slide 40: Imprinting Results
Generally high accuracies across the board
Confusion matrix for whoosh (worst extended test accuracy) on following slide
 | Base Train | Base Test | Extended Train | Extended Test
Push | 98.1% | 99.2% | 91.5% | 80.8%
Pull | 98.9% | 99.0% | 93.8% | 86.0%
Wave | 97.3% | 96.5% | 93.1% | 95.3%
Circle | 94.7% | 94.4% | 79.4% | 88.7%
Whoosh | 96.6% | 96.9% | 72.6% | 78.4%

## Slide 41: Imprinting Results – Whoosh
Train
Test
Base
Extended

## Slide 42: Future Work
Model Improvements:
  Defining a scalar metric based on imprinting results for quantifying model overfitting
  Refine architecture and hyperparameter selection based on overfitting metric
Dataset Improvements:
  Improving data by introducing variability in the collection process, such as new orientation, multiple people
  Dataset pre-processing must be able to handle data cropping and adapt to adjustments within the frames.
Real-time Platform Implementation:
  Identify the hardware and software requirements for implementing an on-the-fly platform for recognizing gestures.

## Slide 43: Future Work
  Model Improvements:
  Implementing deeper networks with ResNet bottlenecks
    Improves feature extraction
  Reducing features in final classification vector
    Decreases overfitting, computational complexity, Currently ~105, target 102 – 103
  Train with weight penalty (L2 regularization)
    Reduces overfitting
    Prevents weights from focusing in on one feature for classification / generates a more general solution
  Train with Adam (optimization algorithm)
    Uses individual learning rate for each parameter.
    Thereby training faster than stochastic gradient method.

## Slide 44: Plans and Deliverables (Year 2/3)
Milestones
  Developed a MATLAB based GUI to streamline raw mmWave radar and IR sensor data collection
  Performed the initial testing of machine learning methods with real mmWave data sets
  Two PhD students (Josiah/Bhaskar) working on various application such as gesture recognition/imaging with 77GHz TI radar until THz radar becomes available
  Students (Richard/Shiva) working on advances machine learning algorithms for dynamic gestures (static gestures before), implemented a flexible python-based infrastructure for gesture recognition using radar information.
  Trained models were investigated for various shortcomings and refined to improve the model robustness.
Deliverables
  Software on the HGR DSP and ML methods (Nov. 15, 2020)
  THz imaging testbed (Nov. 15, 2020)

## Slide 45: Plans and Deliverables (Years 3/4)
Plans
  Extend machine learning/Deep learning methods with new THz sensor
  Software implementation of machine learning algorithms for THz sensing/imaging
  Improve gesture recognition for classifying dynamic gestures (3rd year)
  Present narrowband imaging examples with THz sensor (3rd year)
  Improve the robustness of dynamic gesture classification with confidence metrics (3rd year)
Deliverables
  Report on the results of new applications using mmW demonstrator and multi antenna signal processing and machine learning for hand gesture recognition.
  Software implementation of multi antenna signal processing and machine learning for dynamic hand gesture recognition.

## Slide 46: Advanced Algorithms for Sensing and Recognition: Current Schedule
Year | 1 | 2 | 3 | 4 | 5
Milestones | Develop a detailed mathematical model for THz FPA with reflectors and THz transceivers. Develop a geometric reference model including Doppler shift patterns for 3D gesture recognition and motion detection Software implementation of machine learning algorithms for THz sensing/imaging. | Complete 24/77 GHz hardware demonstrator with existing chipsets to achieve millimeter-scale accuracy in 3D gesture recognition and motion recognition. Develop multi antenna signal processing to reduce speckles and to correct reflector aberration and machine learning techniques. | Software implementation of real-time multi antenna signal processing techniques and machine learning algorithms for THz-FPA on a custom CPU+GPU. Refine the mathematical models of THz-FPA and geometric models based on 77 GHz demonstrator results. | Verify and fine tune low complexity algorithms with THz FPA on silicon with TI and center collaborators. Software implementation of machine learning algorithms on a custom CPU+GPU for THz sensors. Finalize the algorithms to eliminate errors due to multipath. | (If all the milestones are met and authorized by TI) Build and characterize optimized resolution limits of THz FPA with THz chipsets incorporating reflectors and machine learning on CPU/GPU/FPGA for 3D gesture and motion recognition. Characterize the performance limits of aberration mitigation algorithms.
Deliverables | Report on the mathematical model of THz FPA with reflectors and THz radios Report on geometric models for 3D gesture recognition and the machine learning algorithms for THz sensing/imaging | Report on measurement results using 24/77 GHz demonstrator. Software implementation of multi antenna signal processing and machine learning for THz-FPA gesture and motion detection | Report on software implementation and refined mathematical models of the end-to-end sensing and imaging system with machine learning algorithms. Report on the algorithms to increase field of view. | Report on measurement results on the performance limits of multiantenna signal processing algorithms and machine learning techniques used in THz-FPA sensors. | Report on measurement results of fully functional THz-FPA imager enabled by real-time multiantenna signal processing algorithms and machine learning. CPU/GPU/FPGA software.

## Slide 47
Questions ??

## Slide 48: References
[1] H. Kaur and J. Rani, "A review: Study of various techniques of Hand gesture recognition," 2016 IEEE Int. Conf. on Power Electronics, Intelligent Control and Energy Systems, Delhi, 2016, pp. 1-5.
[2] M. K. Ahuja and A. Singh, "Static Vision Based Hand Gesture Recognition Using Principal Component Analysis, " pp. 402-406, 2015.
[3] D. Q. J. Dqg, V. lurp, L. Pdun, O. Kdqg, H. W. Lv, K. Kinect, H. G. Recognition, Z. Fdq, E. H. Fodvvlilhg, E. S. Fodvvlilhuv, and V. Dv, "using Kinect Depth Camera, " pp. 5-8,2015.
[4] J. S. Sonkusare, N. B. Chopade, R. Sor, and S. L. Tade, "A Review on Hand Gesture Recognition System, " 2015 Int. Conf Comput. Commun. Control Autorn., pp. 790-794, 2015.
[5] L. Chen, F. Wang, H. Deng, and K. Ji, "A survey on hand gesture recognition, " 2013 Int. Conf. Comput. Sci. Appl. CSA 2013, pp. 313-316,2013.
[6] S. Atsushi, "Hand Gesture based TV Control System, " Korea -Japan Jt. Work. Front. Comput. Vis., pp. 121-126,2013.
[7] S. Muttena, R. Shiva, S. Sriram, and S. Murugavalli, "Simulation of Speech by Identifying and Classifying Dynamic Gestures, " no. May, pp. 192-197,2015.
[8] J. Chastine, N. Kosoris, and J. Skelton, "A study of gesture-based first person control, " Proc. CGAMES - Int. Conf Comput. Games AI, Animat. Mobile, Interact. Multimedia, Educ. Serious Games, pp. 79-86,2013.
[9] S. S. Rautaray and A. Agrawal, "Vision based hand gesture recognition for human computer interaction: a survey, " Artif. IntelI. Rev., vol. 43, no. 1,2012.
[10] Z. Ren, J. Meng, and J. Yuan, "Depth Camera Based Hand Gesture Recognition and its Applications in Human-Computer-Interaction, " Proc. IEEE Int. Conf Inf Commun. Signal Process., no. I, pp. 3-7, 2011.
[11] J. L. Raheja, M. Minhas, D. Prashanth, T. Shah, and A. Chaudhary, "Robust gesture recognition using Kinect: A comparison between DTW and HMM, " Optik (Stuttg)., vol. 126, no. 11-12, pp. 1098- 1104,2015.
12] L. Xuan and Z. Hong, "An improved canny edge detection algorithm," 2017 8th IEEE International Conference on Software Engineering and Service Science (ICSESS), Beijing, 2017, pp. 275-278.
[13] Z. Zhang, Z. Tian and M. Zhou, "Latern: Dynamic Continuous Hand Gesture Recognition Using FMCW Radar Sensor," in IEEE Sensors Journal, vol. 18, no. 8, pp. 3278-3289, April15, 15 2018.
[14] M. E. Yanik and M. Torlak, “Near-Field MIMO-SAR Millimeter-Wave Imaging With Sparsely Sampled Aperture Data,” IEEE Access, vol. 7, pp. 31801–31819, 2019.

## Slide 49: Backup Slides

## Slide 50: Future Work: Automotive Scene Classification

## Slide 51: Automotive Scene Classification
Radar continuously capturing images from a moving vehicle
Estimate the range of targets in various environments
Target classification: human, stationary object, another vehicle (stationary or moving)
Initial Steps:
Capture dynamic motions with scanner
Classify human movements
Image Courtesy of TI

## Slide 52: Relevant Past Work
3D MIMO-SAR Imaging Algorithms
  Scene generation for segmentation and classification
  Leverage MIMO virtual array elements for larger virtual aperture
Dynamic Gesture Recognition
  Doppler information extraction

## Slide 53: Imprinting Results – Wave
Train
Test
Base
Extended