## Slide 1: Advanced Algorithms for THz Sensing and Recognition
Murat Torlak and Yiorgos Makris
March 1st, 2021 Review

## Slide 2: Outline
New Scanner Construction
2-D Near-Field SAR Imaging
  Simulating the SAR Scenario and Image Recovery
  Super-Resolution with Image Enhancing Network
  Network Training
  Simulation Results
3-D Near-Field SAR Imaging
  Simulating the SAR Scenario and Image Recovery
  Network Training
  Simulation Results
  Real-Data Results
Conclusions and Future Work

## Slide 3: New Scanner Construction

## Slide 4: New Scanner Construction
Mail inspection scanner
  Requires downward-facing imaging system
  Current system is vertically oriented
  Working on a new, versatile system
1m

## Slide 5: New Scanner Construction

## Slide 6: 1-D Scanning 2-D Image Reconstruction

## Slide 7: 2-D Near-Field SAR Imaging
A MIMO sensor is scanned along the y-axis.
The target is a 2-D target in the range (z) and cross-range (y) domains
The echo signal is of the form
The SAR image can be reconstructed using the range migration algorithm (RMA)

## Slide 8: Simulating the SAR Scenario and Image Recovery
Randomly placed point targets
Distortion applied to points is spatially variant
Can we improve the resolution of the recovered image? (“Denoising”)

## Slide 9: Super-Resolution with Image Enhancing Network
Improving SAR image resolution has significant effect on numerous applications: detection, classification, item counting, etc.
Goal: reduce distortion from RMA imaging algorithm using a data-driven approach by training using synthetically generated data
Training:
  Features: recovered images from RMA using simulated data
  Labels: ideal image from simulated data
MIMO Echo Signal
RMA Reconstruction Algorithm
Image Enhancing Network
Better Image!

## Slide 10: Training Data – Synthetic Data
Training Features:
Image of randomly placed point targets recovered using RMA
Training Labels:
Corresponding ideal image. Each point target treated as narrow 2-D Gaussian pulse

## Slide 11: Notes
“Denoising” vs Distortion Removal

## Slide 12: Network Training – Image-to-Image Regression
Features: Distorted Images
Image Enhancement Network
Labels: Ideal Images
The network will learn to remove the distortion from each RMA image to its corresponding ideal image
In this way, the network learns the distortions introduced by the limited aperture effects, spherical wave approximation, limited bandwidth, path loss, etc.

## Slide 13: Network Architecture
Propose a Fully Convolutional Neural Network Approach
  Real-valued 2-D convolution layers, zero-padded to retain image size
  Regression layer output
Training Data
  65536 simulated samples with real radar noise added
    RMA image computed for each sample
    Ideal image computed for each sample
15x15x4 convolution
ReLU Layer
40x40x4 convolution
ReLU Layer
15x15x4 convolution
ReLU Layer
3x3x1 convolution
Clipped ReLU Layer
Regression Layer
In: 256x256x1
Out: 256x256x1

## Slide 14: Results – Random Points
Input to Image Enhancement Network
Output
The network has never seen this target before

## Slide 15: Results – Random Points
Output
Ideal Image – Ground Truth – Label
The network has never seen this target before

## Slide 16: Results – Many Targets
Input to Image Enhancement Network
Output
The network has never seen this target before

## Slide 17: Results – More Targets
Output
Ideal Image – Ground Truth – Label
The network has never seen this target before

## Slide 18: Structured Targets – PSF
Input to Image Enhancement Network
Output
The network has never seen this target before

## Slide 19: Structured Targets – Diamond
Input to Image Enhancement Network
Output
The network has never seen this target before

## Slide 20: Structured Targets – UTD
Input to Image Enhancement Network
Output
The network has never seen this target before

## Slide 21: 2-D Scanning 3-D Image Reconstruction

## Slide 22: 3-D Near-Field SAR Imaging
TI AWR1443 radar using 8 virtual channels simulated
Scanned in planar pattern
3-D target in the near-field
256 x 256 virtual synthetic aperture

## Slide 23: Simulating the SAR Scenario and Image Recovery
Randomly placed point targets
Distortion applied to points is spatially variant

## Slide 24: Training Data – Synthetic Data
Training Features:
Image of randomly placed point target recovered using RMA
Training Labels:
Corresponding ideal image. Each point target treated as narrow 3-D Gaussian pulse
Network trained with 1024 samples of size 128x128x128  Need more computation power

## Slide 25: Results – Random Points
Input to Image Enhancement Network
Output
The network has never seen this target before

## Slide 26: Results – Random Points
Output
Ideal Image – Ground Truth – Label
The network has never seen this target before

## Slide 27: Structured Targets – PSF
Input to Image Enhancement Network
Output
The network has never seen this target before

## Slide 28: Structured Targets – PSF Comparison (dB)

## Slide 29: Structured Targets – Grid of Points
Input to Image Enhancement Network
Output
The network has never seen this target before

## Slide 30: Structured Targets – UTD
Input to Image Enhancement Network
Output
The network has never seen this target before

## Slide 31: Structured Targets – Triangle
Input to Image Enhancement Network
Output
The network has never seen this target before

## Slide 32: Structured Targets – Cutout
Input to Image Enhancement Network
Output
The network has never seen this target before

## Slide 33: Real-Data Results – Knife
Knife handle hidden behind structure holding the knife
Reconstructed image shows the knife blade (notice dynamic range 5dB)

## Slide 34: Real-Data Results – Knife
25 dB
20 dB
10 dB
5 dB
Metal Dots in the handle are now shown (notice dynamic range 25dB)
- Considerable denoising is achieved

## Slide 35: Conclusions and Future Work
Conclusions
Training on synthetic data does generalize to the real-data case
Near-field SAR super-resolution can be achieved using a data-driven approach, drastically improving the sensing ability of imaging systems for numerous applications
Field is ripe for novelty, innovation, and publication
Future Work
Generate more data – Include shapes, points, 3-D objects, etc.
Optimize network architecture and training
  Consider other approaches GANs, sparse CNNs, etc.
Consider various problem statements to improve generalizability
  Parameter, scan size/type agnostic network?
  Introduce further “realistic errors” into the scanning simulation