## Slide 1
Texas Instruments Foundational Technology Research Program on Millimeter Wave and High Frequency Microsystems
42 Month Review
August 6th, 2021

## Slide 2
08:20-08:30 AM Check-in
08:30-09:00 AM Center Progress/Overview
09:00-09:50 AM 0.41-THz CMOS-based Short-Range Imager for Industrial Applications
09:50-10:30 AM Code-Modulated Embedded Test of Multifunctional Arrays
10:30-10:40 AM Break
10:40-11:20 AM Packaging and Material Spectroscopy to Support Terahertz Microsystems
11:20-12:00 PM Infrared Detection Using Structures in Foundry CMOS
12:00-12:10 PM Set up for lunch
12:10-12:50 PM 170GHz – 260GHz Wideband PA and LNA Design in Silicon
12:50-01:30 PM Advanced Algorithms for Terahertz Sensing and Recognition
01:30-02:00 PM Discussion
Texas Instruments Foundational Technology Research Program on Millimeter Wave and High Frequency Microsystems
42 Month Review

## Slide 3
Title of Task
42 Month Review
University Logo
August 6th, 2021

## Slide 4: IR Detection Using Structures in CMOS (First Mandatory Slide)
Description: This project investigates techniques to implement infrared imagers by using electronic detectors fabricated in foundry CMOS that do not need thermal isolation. The read out electronics will be co-integrated with the detectors and the combination will be demonstrated in a package.
Goals: This project seeks to lower the cost of infrared imagers by demonstrating affordably packaged electronic detectors fabricated in foundry CMOS. This project seeks to open up new market opportunities for silicon integrated circuits industry as well as enabling wider uses of IR imaging technology.
Principal Investigator: Kenneth K. O (University of Texas, Dallas)
Students Current Status
Sandeep Kshattry Ph.D. (12/17)
Behnam Pouya Ph.D. (04/20)
Ahsan Ghauri To start in 01/18
Liaisons:

## Slide 5
Plans and Deliverables (Year 4) (2nd to the last Mandatory Slide)
Milestones
Fabricate various junctions (Tape out next week).
Measure and model the junctions including noise performance (May 31st, 2018).
Design 20-THz detectors using various junctions (July 31st, 2018).
Deliverables
Models of junctions (May 31st, 2018).
Report on the design of 20-THz detector (August 31st, 2018).
.

## Slide 6: IR Detection Using Structures in CMOS (Last Mandatory Slide)
 | Year 1 | Year 2 | Year 3 | Year 4
Milestones | -Fabricate various junctions, -Measure and model the junctions including noise performance. -Design 20-THz detectors using various junctions. | -Characterize the detector performance. -Fabricate detectors and arrays with reduced impact of low frequency noise. -Evaluate the impact of packaging on detector performance. | -Fabricate and measure 20 and 40-THz detectors and arrays with an antenna with a larger aperture. -Fabricate, measure, and model alternate detection device test structures. Integrate the detector array in a package with a lens. | -Fabricate and measure 40-THz detectors with an on-chip metamaterial reflector. -Evaluate the packaged detector. Improve meta-material reflector.
Deliverables | -Models of junctions -Report on the design of 20-THz detector | -Report on measurement results of 20-THz detector -Report on performance change due to packaging. | -Report on measurement results of detector array with an increased aperture -New models for junctions. -Report on performance change due to packaging with a lens. | -Report on measurements of 40-THz detector array with an on-chip reflector.

## Slide 7
Developed techniques to measure temperature dependence of dielectric properties. (Mark Lee)
Continue to improve the measurement techniques for low loss-tangent materials at 1-100 GHz. Starting to investigate ring resonator techniques. (R. Henderson)
Established system and methodology for reliable experimental data collection using TI mmWave radars. Improving the synergy between pre-processing and machine learning blocks. (M. Torlak)
Starting to work on dynamic gesture recognition using data sets from TI mmWave radars. (Y. Makris)
Observed polarization dependence of output voltage of detector using Schottky diode at ~20 THz (18.2-21.5 THz). (K. O)
Demonstrated a 410-GHz transceiver imaging pixel occupying an area of 374×380µm2 (W. Choi)
Preparing for tapeout of PA using IHP 130-nm SiGe HBT technology. (A. Babakhani)
Code-modulated test and calibration developed and validated on a 10-GHz array, showing ±0.4dB gain and ±3o phase accuracy. (B. Floyd)
Major Accomplishments (4th 6 months)

## Slide 8
Investigated data-driven approach for high resolution envelope imaging. Developed THz imaging simulator and imaging pipeline for new THz chip.
Major Accomplishments – BULLET POINT

## Slide 9
Outline
Mail inspection scanner
  System Design
  Early Results + Analysis
SAR Resolution Improvement using Machine Learning
  2D SAR Imaging
    Proposed Solution
    Results
  3D SAR Imaging
    Results
  Empirical Results
  Dataset Generation
    Synthetic Data
    Real SAR Images
THz Imager

## Slide 10
Mail Inspection Scanner
Mail inspection scanner
  Requires downward-facing imaging system
  Current system is vertically oriented
  Built new, versatile system
1m
TI 77GHz mmWave Radar
Resolution scales with carrier frequency

## Slide 11
System Design
Dual mode scanner
  Vertical or horizontal orientation
  Simulates mail inspection scanner
  TI 77GHz mmWave radar, currently
  THz imager coming

## Slide 12
Early Results + Analysis
Low Reflectivity Target
  Weak reflection
  Somewhat obscured by interferers
High Reflectivity Target
  Strong reflection
  Easily identifiable
TI 77GHz mmWave Radar
Resolution scales with carrier frequency

## Slide 13
Early Results + Analysis
Higher resolution can improve detection performance and image quality

## Slide 14
SAR Resolution - Motivation
Motivation for higher resolution
  SAR images are blurry and distorted
  Limited bandwidth, aperture effects, etc.
Can we improve the resolution of the recovered image? (“Denoising”)

## Slide 15
2D SAR Imaging
2D Imaging SAR Scanning
  Linear scanning pattern
  2D target
  Recover image using range migration algorithm
    Near-field beamformer
  Resulting raw image is blurry and distorted
Raw RMA Image

## Slide 16
Convolutional Neural Network
  Learns spatial features
  Highly effective on structured images
  Supervised learning
    Synthetically generated features and labels (randomly placed points)
Training Features:
Image of randomly placed point targets recovered using RMA
Training Labels:
Corresponding ideal image. Each point target treated as narrow 2-D Gaussian pulse
Proposed ML Solution

## Slide 17
Proposed ML Solution
Image Enhancement CNN
Features: Raw Distorted Images
Labels: High Resolution Images
The network will learn to remove the distortion from each RMA image to its corresponding ideal image
CNN learns and removes distortions (improves resolution)
  Limited aperture effects, spherical wave approximation, limited bandwidth, path loss, etc.

## Slide 18
Results – Random Points
The algorithm has never seen this target before

## Slide 19
Results – Random Points
The algorithm has never seen this target before

## Slide 20
Results – Point Spread Function (PSF)
The algorithm has never seen this target before

## Slide 21
Results – Diamond
The algorithm has never seen this target before

## Slide 22
Results – UTD
The algorithm has never seen this target before

## Slide 23
3D SAR Imaging
3D Imaging SAR Scanning
  Rectangular scanning pattern
  3D target
  Random points + solid objects

## Slide 24
Results – Random Points
The algorithm has never seen this target before

## Slide 25
Results – Random Points
The algorithm has never seen this target before

## Slide 26
Results – PSF
The algorithm has never seen this target before

## Slide 27
Results – PSF Comparison
The algorithm has never seen this target before

## Slide 28
Results – Grid of Points
The algorithm has never seen this target before

## Slide 29
Results – UTD
The algorithm has never seen this target before

## Slide 30
Results – Triangle
The algorithm has never seen this target before

## Slide 31
Results – Cutout
The algorithm has never seen this target before

## Slide 32
Empirical Results - Knife
The algorithm has never seen this target before
Threshold at 5 dB

## Slide 33
Empirical Results - Knife
The algorithm has never seen this target before
20 dB
10 dB
5 dB
Metal Dots in the handle are now shown (notice dynamic range 25dB)
- Considerable denoising is achieved
25 dB

## Slide 34
Data Generation – Synthetic Data
SAR image simulation pipeline
  Interactive GUI
  Efficient dataset generation
  Flexible for any scanning mode
Journal paper on simulation pipeline in progress

## Slide 35
Data Generation – Simulation Software
Waveform + Array + Scan Setup
Target + Simulation Setup

## Slide 36
Data Generation – Synthetic Data
Introduce array position error in simulation algorithm
Simulate scanner position ambiguity

## Slide 37
Data Generation – Synthetic Data
Array position error
  Some point targets are ill-resolved
  Lost definition of shapes

## Slide 38
CNN Results – No Position Error
The algorithm has never seen this target before

## Slide 39
CNN Results – With Position Error
The algorithm has never seen this target before

## Slide 40
Data Generation – Real SAR Images

## Slide 41
THz Imager