## Slide 1: Application I: Efficient SAR Imaging for Non-Cooperative Scanning Geometries
Josiah Smith

## Slide 2: Motivation – Non-Cooperative Array Imaging
Traditional array imaging techniques require highly controlled positioning for SAR scanning apparatus
Emerging applications require relaxing this constraint
  Smart phone mmWave scanner: mobile threat detection
    ISSUE: limited computation power on cell phone
  Automotive SAR imaging
Challenge:
  Efficient image reconstruction algorithms rely on simple scanning patterns
  Non-cooperative scanning patterns are typically considered infeasible due to computational expense
Traditional Array Imaging: Controlled Scanning Pattern

## Slide 3: Multi-Planar Array Concept
2-D Multi-Linear Case:
Captures along different lines
3-D Multi-Planar Case:
Captures along different planes
Rx
Tx
Rx
Tx
Target
Target

## Slide 4: Multi-Planar Array Compensation
Rx
Tx
Target
Problem Statement:
Can we compensate MIMO multi-planar data to resemble SISO planar data at plane?

## Slide 5: Signal Model
Two-way range from Tx/Rx pair
Taylor series expansion around :
Rx
Tx

## Slide 6: Signal Model (cont.)
FMCW beat signal from the Tx/Rx pair
Equivalent beat signal from virtual SISO element at the plane
Compensation is simple phase compensation!

## Slide 7: Algorithm Comparison
RMA
Recovered Image
BPA
Recovered Image
RMA
Recovered Image
Phase Compensation

## Slide 8: Simulation Results
Multi-Linear Array – Point Targets
BPA – 5 mins
RMA – 30 ms
Ours – 30 ms
Antenna perturbance: Gaussian

## Slide 9: Simulation Results
Multi-Planar Array – Cutout
2-D BPA – 3 hrs
3-D BPA – 150 hrs
RMA – 1 s
Ours – 14 s
Ours – 1 s

## Slide 10: System Design
Multi-Planar Array – Emulate Non-cooperative Geometry
Perform multiple planar scans with the target at different planes
Sample from different scans to emulate non-cooperative geometry
  Take samples from random plane
  Non-cooperative scanning patterns are typically considered infeasible due to computational expense
Compare algorithm performance
  Computational complexity
  Image quality

## Slide 11: Real Results
Multi-Planar Array – Cutout
2-D BPA – 3 hrs
3-D BPA – 150 hrs
Ours – 14 s
Ours – 1 s
Antenna perturbance: Uniform Random
RMA – 1 s

## Slide 12: Real Results
Multi-Planar Array – Cutout
2-D BPA – 3 hrs
3-D BPA – 150 hrs
Ours – 14 s
Ours – 1 s
Antenna perturbance: Emulated Freehand
RMA – 1 s

## Slide 13: Conclusions and Summary
 | BPA | RMA | Ours
Computational Complexity |  |  | 
Image Quality | Acceptable | Unacceptable | Acceptable
Sample Image |  |  | 
 | BPA | RMA | Ours
Computational Complexity |  |  | 
Image Quality | Acceptable | Unacceptable | Acceptable
Sample Image |  |  | 
Enables non-cooperative image computation on mobile devices, cell phones, IOT applications
Same computational complexity as RMA with comparable image quality to BPA

## Slide 14: Application II Vital Sign Detection
Bhaskar Upadhyay

## Slide 15: Agenda
Background
Problems
Proposed solutions
Results
Future direction

## Slide 16: Motivation – Why non-contact vital signs detection?
Commercial vital sign (heart rate and respiration) detection systems traditionally wearable
Not feasible in all scenarios
  Track vital signs of bed ridden patients to detect problems in breathing and sudden changes in heart rate
    Even more important in case of burn victims and newborn babies
Applicable to numerous scenarios:
  Track vital signs of drivers
  Locating survivors in search and rescue missions

## Slide 17: Vital Signs Detection Using FMCW Radars
Transmit a FMCW chirp signal
Signal reflected from subject and a delayed version is received by the receiver
The two are ‘mixed’, giving an IF signal, which contains information about the range and location of the subject
The phase changes caused by breathing and heart rates evaluated to extract vital signs
After ADC sampling, the IF signal at receive element is
Range
Angle
Breathing
Heartbeat
FMCW Signal

## Slide 18: Problems
Respiration
Harmonics
Intermodulation Products
Spurs
Sub mm scale vibrations
Low SNR of heart signal
Harmonics
Intermodulation products
Motion artifacts
Single channel systems and algorithms not robust
Weak Heart Signal
Heart Rate (bpm)
Time (s)
60
70
80
*
*
*
*
*
*
*
*
*
*
*
*

## Slide 19
Proposed Solution 1 – MIMO Rx Beamforming Based
Proposed Solution 2 – RF Lens Based
Radar
Radar
Lens

## Slide 20
People Counting
Search and Rescue
Driver fatigue
Sleep Monitoring
Proposed Solution 1 – MIMO Rx Beamforming Based
Proposed Solution 2 – RF Lens Based

## Slide 21: System Parameters
Parameter (FMCW) | Value
Number of Samples (fast time) | 128
Number of Frames (slow time) | 512
Frequency | 77 GHz
Bandwidth (BW) | 4 GHz
PRF (Slow Time) | 20 Hz
NRx antennas | 4
NTx antennas | 2
Measurement Time 25 s

## Slide 22: Proposed Solution 1 – MIMO Rx Beamforming Based – Results
a. Vital Signs Spectrum
b. Vital Signs Pseudo Spectrum
c. Heart Rate Tracking Across Time
e. Bland-Altmann Plot
Mean Absolute Error (MAE) – 1.69 bpm
Accuracy – 91.85 %

## Slide 23: RF Lens Based Solution – Lens Cage Experiments
LAT-115 Lens
DCA1000EVM
AWR1843BOOST
3D Printed Lens Cage System
1
2
3
4
Lens placed at a distance in front of sensor (back focal length of the lens)
3D printed lens cage designed for stability and movement
Subjects positional analysis done to identify capability of heart rate detection
SNR improvements due to the lens
Focusing property and lens geometry helps resolve echoes from different points on the body
Channel selection based on spectral PAPR
“Need based” Harmonic correction implemented
Don’t select this channel!
Select this channel!

## Slide 24: Heart Rate Visibility Different Orientations of subject
Heart rate visible for all positions
Peak strength varies
Lens based approach can be applied for applications with positional changes
  Sleep monitoring
Heart rate peak

## Slide 25: Heart Rate Tracking Still subject facing sensor
Heart Rate Tracking Across Time
Limited experiments, promising results
Subject still
Accuracy 90 % (at optimal points)

## Slide 26: Summary of Pilot Studies
Combining Technique | Max Peak Isolated
Non Coherent | 
Rx – Beamforming + PAPR Condition on angle bin | 
Combining Technique | Max Peak Isolated
Rx – Beamforming + PAPR Condition on angle bin | 
Combining Technique | Max Peak Isolated
Rx Beamforming Peak Tracking and Counting | 
Mean Absolute Errors | 1.69 bpm
Combining Technique | Max Peak Isolated
Rx Beamforming Peak Tracking and Counting | 
Mean Absolute Errors | 1.69 bpm
Current Problems
  Motion corruption increases progressively from laying down to sitting to standing positions.
  Artifacts of small scale body motion appear at vital sign frequencies.
Current Research
  Time frequency analysis to resolve and remove effect of motion.
  Utilize algorithm for real time application with motion.
Goal
  Make algorithm robust even against motion.
Use of lens improves vital signs detection
Doppler Peak to Average Power Ratio (PAPR) method utilized for channel selection.
With harmonic check algorithm added, accuracy increases further. (> 90%)
Both solutions are worth exploring – use depends on application case