## Slide 1: Confidentiality
By reviewing this presentation or participating in a SRC event, you are agreeing not to use the presented information for purposes unrelated to the event until approved by SRC;
Material may be presented that represents current research, some of which has not been published or protected. This material is not for public disclosure and until potential IP rights have been protected, please treat all of the information presented as confidential information which is the property of the researcher and their university.

## Slide 2: Novel Super-Resolution and MIMO Techniques for Automotive and Emerging Radar Applications
Murat Torlak, UT Dallas
SRC Task 2712.029

## Slide 3: Novel Super-Resolution and MIMO Techniques for Automotive and Emerging Radar Applications 2712.029, Murat Torlak, University of Texas at Dallas
Technical Thrust: Analog/Mixed-Signal Circuits, Systems, and Devices (AMS-CSD)
Task Leader: Murat Torlak, Professor, University of Texas at Dallas
Industrial Liaisons: Dan Wang (Texas Instruments)
Anticipated Results: Algorithms which utilize the hardware efficiently and produce robust estimation of high resolution radar images in complex environments.
Task Description: Develop novel super-resolution and MIMO techniques to achieve high-performance and low complexity for automotive and emerging radar applications.
Task Deliverables: (1) Development of mathematical models of the proposed robust and low complexity high resolution imaging techniques and their software implementation (2) MIMO mathematical models and software implementation
Start Date: Aug. 2017

## Slide 4: Students on Task 2712.029
Graduated Students and Current Affiliation
  Dr. Muhammet Emin Yanik, May 2020
Current Students and Anticipated Graduation Date
  Ashwin Bhobani Baral, Aug 2021
  Bhaskar Raj Upadhyay, Aug 2022
  Josiah Wayland Smith, Aug 2022
Internships and Full-Time Offers
  Muhammet Emin Yanik, TI, Full-time (Jan’20)
  Josiah Wayland Smith, Imec, Internship, Sum’20

## Slide 5: Executive Summary
Accomplishments during the past year
  Completed 2D mmWave Fast SAR imager
  Developed 3D MIMO-ISAR imaging testbed/algorithms
  Developed vital sign monitoring algorithms
Future direction – highlighting changes
  Development of real-time MIMO algorithms for increasing detection and tracking accuracy in dynamic time-variant and multipath environments
  Demonstration of mm-Wave radar technology in-home monitoring/fall detection and for video game players

## Slide 6: Motivation and Agenda
mmWave imaging technology is one of the fastest growing technologies of this decade with wide range of applications.
  Security screening, Vital sign monitoring, Gesture recognition,
  Automotive radars, Smart homes, UAV radars and imaging
Application I: mmWave MIMO-ISAR Imaging prototype
  System model and algorithms
  Based on TI 77 GHz mmWave radar sensors
  Mechanical scanner
  Experimental Results
Application II: Vital Sign Detection
  Algorithms verified via pendulum/speakers
  Pilot experiments
Publications/Ongoing Work and Future Directions

## Slide 7: Application I: Efficient SAR Imaging for Non-Cooperative Scanning Geometries
Josiah Smith

## Slide 8: Motivation – Non-Cooperative Array Imaging
Traditional array imaging techniques require highly controlled positioning for SAR scanning apparatus
Emerging applications require relaxing this constraint
  Smart phone mmWave scanner: mobile threat detection
    ISSUE: limited computation power on cell phone
  Automotive SAR imaging
Challenge:
  Efficient image reconstruction algorithms rely on simple scanning patterns
  Non-cooperative scanning patterns are typically considered infeasible due to computational expense
Traditional Array Imaging: Controlled Scanning Pattern

## Slide 9: Multi-Planar Array Concept
2-D Multi-Linear Case:
Captures along different lines
3-D Multi-Planar Case:
Captures along different planes
Rx
Tx
Rx
Tx
Target
Target

## Slide 10: Multi-Planar Array Compensation
Rx
Tx
Target
Problem Statement:
Can we compensate MIMO multi-planar data to resemble SISO planar data at plane?

## Slide 11: Signal Model
Two-way range from Tx/Rx pair
Taylor series expansion around :
Rx
Tx

## Slide 12: Signal Model (cont.)
FMCW beat signal from the Tx/Rx pair
Equivalent beat signal from virtual SISO element at the plane
Compensation is simple phase compensation!

## Slide 13: Algorithm Comparison
RMA
Recovered Image
BPA
Recovered Image
RMA
Recovered Image
Phase Compensation

## Slide 14: Simulation Results
Multi-Linear Array – Point Targets
BPA – 5 mins
RMA – 30 ms
Ours – 30 ms
Antenna perturbance: Gaussian

## Slide 15: Simulation Results
Multi-Planar Array – Cutout
2-D BPA – 3 hrs
3-D BPA – 150 hrs
RMA – 1 s
Ours – 14 s
Ours – 1 s

## Slide 16: System Design
Multi-Planar Array – Emulate Non-cooperative Geometry
Perform multiple planar scans with the target at different planes
Sample from different scans to emulate non-cooperative geometry
  Take samples from random plane
  Non-cooperative scanning patterns are typically considered infeasible due to computational expense
Compare algorithm performance
  Computational complexity
  Image quality

## Slide 17: Real Results
Multi-Planar Array – Cutout
2-D BPA – 3 hrs
3-D BPA – 150 hrs
Ours – 14 s
Ours – 1 s
Antenna perturbance: Uniform Random
RMA – 1 s

## Slide 18: Real Results
Multi-Planar Array – Cutout
2-D BPA – 3 hrs
3-D BPA – 150 hrs
Ours – 14 s
Ours – 1 s
Antenna perturbance: Emulated Freehand
RMA – 1 s

## Slide 19: Conclusions and Summary
 | BPA | RMA | Ours
Computational Complexity |  |  | 
Image Quality | Acceptable | Unacceptable | Acceptable
Sample Image |  |  | 
 | BPA | RMA | Ours
Computational Complexity |  |  | 
Image Quality | Acceptable | Unacceptable | Acceptable
Sample Image |  |  | 
Enables non-cooperative image computation on mobile devices, cell phones, IOT applications
Same computational complexity as RMA with comparable image quality to BPA

## Slide 20: Application II Vital Sign Detection
Bhaskar Upadhyay

## Slide 21: Motivation – Why non-contact vital signs detection?
Commercial vital sign (heart rate and respiration) detection systems traditionally wearable
Not feasible in all scenarios
  Track vital signs of bed ridden patients to detect problems in breathing and sudden changes in heart rate
    Even more important in case of burn victims and newborn babies
Applicable to numerous scenarios:
  Track vital signs of drivers
  Locating survivors in search and rescue missions

## Slide 22: Vital Signs Detection Using FMCW Radars
Transmit a FMCW chirp signal
Signal reflected from subject and a delayed version is received by the receiver
The two are ‘mixed’, giving an IF signal, which contains information about the range and location of the subject
The phase changes caused by breathing and heart rates evaluated to extract vital signs
After ADC sampling, the IF signal at receive element is
Range
Angle
Breathing
Heartbeat
FMCW Signal

## Slide 23: Vital Signs Detection Using mmWave Radars
Evaluation scheme
Single chirp samples (fast time) to resolve subject in range
Multi channel transmit and receive to resolve subject in angle (virtual channels)
Evaluate echo signal from subject across time (slow) to resolve vital signs

## Slide 24: Problems
Respiration
Harmonics
Intermodulation Products
Spurs
Sub mm scale vibrations
Low SNR of heart signal
Harmonics
Intermodulation products
Motion artifacts
Single channel systems and algorithms not robust
Weak Heart Signal
Heart Rate (bpm)
Time (s)
60
70
80
*
*
*
*
*
*
*
*
*
*
*
*

## Slide 25
Proposed Solution 1 – MIMO Rx Beamforming Based
Proposed Solution 2 – RF Lens Based
Radar
Radar
Lens

## Slide 26
People Counting
Search and Rescue
Driver fatigue
Sleep Monitoring
Proposed Solution 1 – MIMO Rx Beamforming Based
Proposed Solution 2 – RF Lens Based

## Slide 27: System Parameters
Parameter (FMCW) | Value
Number of Samples (fast time) | 128
Number of Frames (slow time) | 512
Frequency | 77 GHz
Bandwidth (BW) | 4 GHz
PRF (Slow Time) | 20 Hz
NRx antennas | 4
NTx antennas | 2
Measurement Time 25 s

## Slide 28: Proposed Solution 1 – MIMO Rx Beamforming Based – Results
a. Vital Signs Spectrum
b. Vital Signs Pseudo Spectrum
c. Heart Rate Tracking Across Time
e. Bland-Altmann Plot
Mean Absolute Error (MAE) – 1.69 bpm
Accuracy – 91.85 %

## Slide 29: RF Lens Based Solution – Lens Cage Experiments
LAT-115 Lens
DCA1000EVM
AWR1843BOOST
3D Printed Lens Cage System
1
2
3
4
Lens placed at a distance in front of sensor (back focal length of the lens)
3D printed lens cage designed for stability and movement
Subjects positional analysis done to identify capability of heart rate detection
SNR improvements due to the lens
Focusing property and lens geometry helps resolve echoes from different points on the body
Channel selection based on spectral PAPR
“Need based” Harmonic correction implemented

## Slide 30: Verifying Region of Focus Corner Reflector
Total x-axis motion = 50 cm
Total y-axis motion = 40 cm
Approximate 6 dB deviation from maximum at ~ 6 cm
If the object moves from one point to the next (from to ) The position of image also moves (from to )
From and
What the Rx antenna sees at each of these points is a fraction of the intensity based on the location of the Point Spread Function
Different RX’s dominated by signal coming off different points in the torso

## Slide 31: SNR gain and channel variation with lens
Rx 1
Ground value: ~86 bpm
With lens – High deviations in spectrum across receivers
Rx 2
Rx 3
Rx 4
Rx 1
Rx 2
Rx 3
Rx 4
With Lens
Without Lens

## Slide 32: Channel selection – Spectral Peak to Average Power Ratio (PAPR method)
Within this region:
Compute the Peak to Average Power Ratio
Red line denotes the ground value
Select channel 2
Consider the estimate of selected channel as heart rate estimate

## Slide 33: Heart Rate Visibility Different Orientations of subject
Heart rate visible for all positions
Peak strength varies
Lens based approach can be applied for applications with positional changes
  Sleep monitoring
Heart rate peak

## Slide 34: Heart Rate Tracking Still subject facing sensor
Heart Rate Tracking Across Time
Limited experiments, promising results
Subject still
Accuracy 90 % (at optimal points)

## Slide 35: Heart Rate Tracking Still subject facing sensor
Heart Rate Tracking Across Time
Limited experiments, promising results
Subject still
Accuracy 90 % (at optimal points)

## Slide 36: Summary of Pilot Studies
Combining Technique | Max Peak Isolated
Non Coherent | 
Rx – Beamforming + PAPR Condition on angle bin | 
Combining Technique | Max Peak Isolated
Rx – Beamforming + PAPR Condition on angle bin | 
Combining Technique | Max Peak Isolated
Rx Beamforming Peak Tracking and Counting | 
Mean Absolute Errors | 1.69 bpm
Combining Technique | Max Peak Isolated
Rx Beamforming Peak Tracking and Counting | 
Mean Absolute Errors | 1.69 bpm
Current Problems
  Motion corruption increases progressively from laying down to sitting to standing positions.
  Artifacts of small scale body motion appear at vital sign frequencies.
Current Research
  Time frequency analysis to resolve and remove effect of motion.
  Utilize algorithm for real time application with motion.
Goal
  Make algorithm robust even against motion.
Use of lens improves vital signs detection
Doppler Peak to Average Power Ratio (PAPR) method utilized for channel selection.
With harmonic check algorithm added, accuracy increases further. (> 90%)
Both solutions are worth exploring – use depends on application case

## Slide 37: Dissemination Activities
Industry interactions
  Monthly reviews with Texas Instruments
  Project discussions with liaisons at TI
  SRC Annual reports and publications
  SRC e-seminars
TxACE talks
IEEE Special Issue on Automotive Radars
Conference presentations
Techcon submissions
Nominated for the best paper award in IEEE SP Magazine

## Slide 38: Publications
M. Yanik, D. Wang and M. Torlak, “3-D MIMO-SAR Imaging Using Multi-Chip Cascaded Millimeter-Wave Sensors,” Proc. IEEE Globalsip Conf., Nov. 11-14, 2019, Ottawa, Canada.
M. Yanik, D. Wang and M. Torlak, "Development and Demonstration of MIMO-SAR mmWave Imaging Testbeds," IEEE Access, vol. 8, pp. 126019-126038, July 8, 2020.
J. W. Smith, M. Yanik, and M. Torlak, “Near-Field MIMO-ISAR Millimeter-Wave Imaging, Proc. IEEE Radar Conf., Sept. 21-25, 2020, Florence, Italy.
A. B. Baral and M. Torlak, “Joint Doppler Frequency and Direction of Arrival Estimation for TDM MIMO Automotive Radars,” IEEE Journal of Sel. Topics in Signal Proc., Sept. 2020, submitted.
Guest Editor, IEEE JSTSP Special Issue on Recent Advances in Automotive Radar Signal Processing