## Slide 1
TxACE
mmWave Radar for Gesture Recognition
Josiah W. Smith
In collaboration with:
Dr. Torlak, Dr. Makris
S. Thiagarajan, B. Upadhyay, R. Willis
University of Texas at Dallas
February 13th, 2019

## Slide 2: Hand Gesture Recognition
Goal: Demonstrate real-time hand gesture recognition using FMCW mmWave radar
  For future application with THz imager
Investigate how the back-scattered signal changes due to dynamic (motion) hand gestures
Develop MATLAB application to collect large hand gesture signal data sets
Identify features which are suitable for scattered radar waveforms and immune to the background noise
Develop fine-grain signal processing based on space-range-Doppler analysis to improve machine learning accuracy

## Slide 3: Outline
FMCW Basics
Static Data Collection Applications
Static Hand Gesture Recognition
  Old Setup
  New Setup
Conclusions and Future Work

## Slide 4
FMCW Basics

## Slide 5: FMCW Chirp
Chirp Signal
  Frequency increases with time
Frequency Versus Time

## Slide 6: Signal Flow
Transmitted signal is mixed with received signal
IF signal send through a lowpass filter and an ADC
, ,
,

## Slide 7: FT of Received Signal
Time-frequency plot of chirp and received chirp
Single reflection results in one peak in frequency/range domain

## Slide 8: FT of Received Signal
Multiple reflections result in multiple peaks in the range domain.
For gesture case, many peaks and noise can be seen in the range spectrum.

## Slide 9: Range Analysis
Range spectrum

## Slide 10
Static Data Collection Applications

## Slide 11: MATLAB HGR App
Detailed control over radar settings and configuration
High-Speed LVDS Interface will allow for transfer of raw data without HSDC.
In testing phase, we are improving automation and real-time programs

## Slide 12: Automation through MATLAB App
App capable of collecting an arbitrary number of captures as needed
Specify periodicity of capture for bulk capturing of data
Load data and save directly from GUI

## Slide 13: MATLAB HGR App
Capture data and display the prediction
2D FFT
Comparison of methods
Select range for comparison
Uses multiple neural networks for classification
Preprocessing to emphasize characteristics

## Slide 14
Static Hand Gesture Recognition

## Slide 15: Static Hand Gestures
Fist
Two
Palm
C
Perpendicular (perp)
Thumbs Up (tu)

## Slide 16: OLD Static Experiment Parameters
Using TI mmWave radar equipment is set up specifically for hand gesture data collection.
Samples are taken of each hand static gesture from a distance of 0.4m to 0.5m from radar with a constant, distant background.
Five gestures are used in addition to a ‘none’ gesture (without any hand in the specified range)
Radar Parameters:
  1 TX, 4 RX
  16bit, Complex1x
  Start Frequency: 77GHz Old Maximum Range:
  Bandwidth: 3.99948GHz Rmax = 21.58m
  Slope: 63.343 Hz/s
  ADC Samples: 512
  Sample Rate: 9121 ksps

## Slide 17: OLD Static Data Collection
Using automation program, collection of bulk data for maximum independence among captures
Distance from sensor varied from 0.4m to 0.5m
Angle with respect to sensor varied approximately ±30° in every direction
Start Lower Angled Angled

## Slide 18: OLD Results
Neural network training with large, varied datasets
89.55% Accuracy with layered imaginary and real parts

## Slide 19: NEW Static Experiment Parameters
Using TI mmWave radar equipment is set up specifically for hand gesture data collection.
Samples are taken of each hand static gesture from a distance of 0.35m to 0.55m from the radar with a constant, distant background.
Six gestures are used in addition to a ‘none’ gesture (without any hand in the specified range)
Radar Parameters:
  3 TX, 4 RX (12 Virtual MIMO Channels)
  16bit, Complex1x
  Start Frequency: 77GHz New Maximum Range:
  Bandwidth: 3.99948GHz Rmax = 3m
  Slope: 99.987 Hz/s
  ADC Samples: 64
  Sample Rate: 2000 ksps

## Slide 20: New Setup
Horizontal orientation
25 hand locations
35-55cm range
  Increments of 5cm
  Azimuth angles of 7°
  and 14° on either side
Little to no variation
vertically

## Slide 21: New Setup
As shown below, capture FOV ranges from 35-55cm
across a FOV of
28°, at increments
of 5cm.
14°
7°
7°
14°
35cm
5cm
55cm

## Slide 22: Degrees of Freedom
30° of rotation in each direction
  Side to side
  Forward and backward
  Left and right
Different hands used (different reflectivity etc.)
30°
30°

## Slide 23: Degrees of Freedom
30°
30°
30°
30°

## Slide 24: New Raw Range Data

## Slide 25: New Raw Range Data

## Slide 26: Preliminary CNN
Neural network training with preliminary, small dataset
94.17% Accuracy with layered imaginary and real parts

## Slide 27: Preprocessing
Increased FFT size
  Increases number of features from which machine learning algorithm can choose
Complex Normalization
  Average the data across captures
  Find maximum of average for each channel
  Normalize by the complex value of this maximum
  Normalize to zero mean and unit variance

## Slide 28: New Normalized Data

## Slide 29: New Normalized Data

## Slide 30: CNN with Normalized Data
Neural network training with preliminary, small dataset
96.54% Accuracy with layered imaginary and real parts

## Slide 31: Time-Freq Preprocessing
Short Time Fourier Transform (STFT) and Continuous Wavelet Transform (CWT)
  To utilize time-frequency components
Fourier Synchrosqueezing Transform (FSST)
  Circumvents uncertainty relations found in STFT and CWT [2]

## Slide 32: CNN with FSST Normalized Data
Neural network training with preliminary, small dataset
97.84% Accuracy with layered imaginary and real parts

## Slide 33: Conclusions and Future Work
Static gesture recognition
  Updated settings producing increased accuracy
  Automated data collection to obtain large data sets
  Preprocessing techniques (normalization, FSST) improving accuracy by emphasizing features
  Real-time system coming soon
Dynamic gesture recognition
  Once static case is optimized
  Doppler information utilized
  High resolution should yield high accuracy
Sub-millimeter radar using THz imager

## Slide 34: References
  [1] S. Rao, "Introduction to mmwave Sensing: FMCW Radars", Texas Instruments.
  [2] A. Wojciechowska, "Usage des archives ouvertes dans les domaines des mathématiques et de l'informatique", Documentaliste-Sciences de l'Information, vol. 43, no. 5, p. 294, 2006. Available: 10.3917/docsi.435.0294.

## Slide 35
TxACE
mmWave Radar for Gesture Recognition
Josiah W. Smith
In collaboration with:
Dr. Torlak, Dr. Makris
S. Thiagarajan, B. Upadhyay, R. Willis
University of Texas at Dallas
February 13th, 2019

## Slide 36: Excess Slides
  Not to be used

## Slide 37
Dynamic Hand Gestures

## Slide 38: Dynamic Hand Gesture Recognition
Consider two dynamic hand gestures, pushing (down) and pulling (up)
We expect the pushing (down) motion to result in a positive velocity as it is coming towards the radar.
Similarly, we expect the pulling (up) motion to result in a negative velocity.
Pulling
Pushing
RADAR

## Slide 39: Space-Range-Doppler Analysis
Multi-dimensional frequency analysis
The received back-scattered signal (complex) can be denoted as
  Where is the virtual antenna index (due to different tx transmission);
  is the range frequency bin; and
  is the slow-time index
Data cube

## Slide 40: Doppler Processing
Pulling up vs pushing down

## Slide 41: Dynamic Hand Gesture Example
Range Frequency-Slow Time Analysis

## Slide 42: Dynamic Results
Neural network training with
97.31% Accuracy considering only magnitude of response

## Slide 43
Infrared Gesture Recognition

## Slide 44: IR images of static hand gestures
Two
Palm
Perpendicular
Fist
Curl

## Slide 45: Live HGR with IR Sensors
Real-time IR-based gesture recognition using a convolutional neural network

## Slide 46: Radar Waveform Selection for Imager
Pulsed waveforms, i.e., FSK
Chirp (FMCW)
Stepped Frequency Waveforms
Unambiguous range

## Slide 47: Transmitted Signal
Chirp Signal is in the form:
TX Signal:
Signal is repeated Nchirps times with a periodicity of TF
Transmitted signal sent from TX antenna and
signal received back 𝜏 seconds later.
Signals are mixed to produce IF signal
(note: Π is the unit rectangle function)

## Slide 48: Received Signal
From one chirp, received signal comes in the form:
Therefore

## Slide 49: Received Signal
Mixed with the TX signal then sent through a LPF
a single tone signal

## Slide 50: FT of Received Signal
As shown to the left, the frequency of the received signal is time delayed 𝜏 seconds.
Multiple Reflections from objects

## Slide 51: FT of Mixed Signal
Zeros: , Center Middle Frequency:

## Slide 52: Multiple Reflections
For multiple reflections, the range/frequency spectrum shows peaks at multiple range bins. Each gesture’s frequency response has minor differences from each channel perspective