## Slide 1: Radar Perception for Gesture Recognition
Josiah W. Smith
Advisor: Dr. Murat Torlak
Special thanks to: Shiva Thiagarajan, Richard Willis, Bhaskar Upadhyay, Dr. Muhammet Yanik

## Slide 2: Outline
Static Hand Gesture Recognition
  Setup and data format
  Preprocessing techniques
  Results
Dynamic Hand Gesture Recognition
  Setup and data format
  Preprocessing techniques and cost efficiency analysis
Interfacing with Terahertz Sensor IC
  Submillimeter relative range estimation
Conclusions and Future Work

## Slide 3: Static Hand Gesture Recognition

## Slide 4: Static Hand Gestures
Fist
Two
Palm
C
Perpendicular (perp)
Thumbs Up (tu)

## Slide 5: Setup and Degrees of Freedom
As shown below, capture FOV ranges from 35-55cm across a FOV of 28°, at increments of 5cm.

## Slide 6: Static Data Format
At each location, one capture is made per hand orientation
Each capture consists of 64 frames, only the first fame is used
100 captures = 4 different hand orientations at each of the 25 locations
Radar Parameters:
  3 TX, 4 RX (12 Virtual MIMO Channels)
  16bit, Complex1x
  Start Frequency: 77GHz
  Bandwidth: 3.99948GHz
  Rmax = 3m
  Slope: 99.987 Hz/s
  Sample Rate: 2000 ksps

## Slide 7: Range FFT of Received Signal
Multiple reflections result in multiple peaks in the range domain [1].
For gesture case, many peaks and noise can be seen in the range spectrum.

## Slide 8: Static Datasets
Dataset 1: 2000/class
  Same location at radar bore side
  Single subject, across several weeks
  83% Accuracy
Dataset 2: 4000/class
  Ranges 35cm-55cm and 28° FOV
  3 subjects, hand too close to torso
  61% Accuracy
Dataset 3: 405/class
  Ranges 45cm-55cm and 14° FOV
  Hand held away from torso
  86% Accuracy

## Slide 9: Range FFT Format
Range FFT produces a 12 x N array with 12 virtual channels and N range bins
...
...
...
Channel 1
Channel 2
Channel 3
Channel 4
Channel 5
Channel 6
Channel 7
Channel 8
Channel 9
Channel 10
Channel 11
Channel 12
R1 | R2
RN

## Slide 10: Reformatting Range FFT to 3D
Reformatted Range FFT to align with virtual array produces array of size 8 x N x 2
...
Channel 1
Channel 2
Channel 3
Channel 4
Channel 9
Channel 10
Channel 11
Channel 12
R1 | R2
RN
...
Zero Pad
Zero Pad
Channel 5
Channel 6
Channel 7
Channel 8
Zero Pad
Zero Pad
Notes: Make slide about real/complex layering of machine learning network

## Slide 11: 3D Range-Angle FFT
After Range-FFT, another FFT is performed across the sensor dimension to produce the Range-Angle FFT.
The angle domain shows a peak at the azimuth angle of arrival for returning chirp signals.
We will consider a region of the Angle-Range FFT in which we expect the gesture to appear.
...
R1 | R2
...
Dimension 1
Dimension 2
RN

## Slide 12: Preprocessing Techniques
Data formatting
  Layer real and imaginary parts
  Leverage relative phase differences between channels by maintaining matrix format rather than vectorizing data
  Drastic accuracy increase
Null Torso Peak
  Attempt to remove torso peak and sidelobes
  Some accuracy reduction, revisit
Range-Channel Autocorrelation
  2D correlate to create spatial invariance
  No change in accuracies, revisit

## Slide 13: Preprocessing Results
Range-Angle FFT
  Reformat data with prior knowledge of virtual array structure
  Exploit both elevation and azimuth information
  Increase in accuracy
 | Dataset 1 | Dataset 2 | Dataset 3
Raw | 83% | - | -
Reformatted | 95% | 61% | 86%
Nulled | - | 61% | 80%
Autocorr | 95% | 62% | 87%
Range-Angle FFT | 99% | 75% | 91%

## Slide 14: Dynamic Hand Gesture Recognition

## Slide 15: Dynamic Hand Gestures
Circle
Whoosh
Pull
Push
Wave

## Slide 16: Dynamic Data Collection Setup
Chest high radar
~1m from sitting user
Simple range FFT computed for each capture
Radar Parameters:
  3 TX, 4 RX (12 Virtual MIMO Channels)
  16bit, Complex1x
  Start Frequency: 77GHz
  Bandwidth: 3.99948GHz
  Rmax = 3m
  Slope: 99.987 Hz/s
  Sample Rate: 2000 ksps
  64 Fast Time Samples

## Slide 17: Preprocessing Techniques: Angle FFT
Channel to azimuth angle domain
Considering geometry of aperture, FFT across channel domain produces angular domain
16 Angle Bins
Filter angular domain to effectively achieve RX beamforming

## Slide 18: Preprocessing Techniques: Doppler (Velocity) FFT
Negative
Velocity
Positive
Velocity

## Slide 19: Preprocessing Techniques: STFT

## Slide 20: Dynamic Dataset: Results and Size
Dataset 4 – 600/class
  512 frames over 2.56s (5ms PRI)
  Captured across different days, same subject
Size of data for each class (64, 12, 512, 600)
  64: range bins (25 bins containing torso and hand)
  12: virtual antennas
  512: slow-time (frame index)
  600: captures/class

## Slide 21: 3-Tx, 4-Rx Channels Used
Preprocessing Technique
Range FFT
Range, Doppler
Range, Doppler Filtered
Range, Angle
Range, Angle, Doppler Filtered
Range FFT, Doppler STFT Filtered
Range, Angle, Doppler STFT Filtered
Data Size / Class
(25, 12, 512, 600)
(25, 12, 512, 600)
(25, 12, 64, 600)
(25, 16, 512, 600)
(25, 16, 64, 600)
(25, 12, 13, 64, 600)
(25, 16, 13, 64, 600)
Efficiency
98.8% / 28ms
99.2% / 29ms
98.2% / 15ms
99% / 16ms
99.2% / 19ms
97.5% / 25ms
98.8% / 28ms

## Slide 22: First Channel Only (More Efficient)
Preprocessing Technique
Range FFT
Range, Doppler
Range, Doppler Filtered
Range FFT, Doppler STFT Filtered
Range FFT 40ms PRI (subsampled)
Range, Doppler 40ms PRI
Data Size / Class
(25, 1, 512, 600)
(25, 1, 512, 600)
(25, 1, 64, 600)
(25, 1, 13, 64, 600)
(25, 1, 64, 600)
(25, 1, 64, 600)
Efficiency
98.5% / 9ms
99.5% / 10ms
98.8% / 8.5ms
99.3% / 9ms
98.5% / 9ms
98.5% / 9.2ms

## Slide 23: Subsample from 5ms PRI to 40ms PRI
Preprocessing Technique
Range FFT 40ms PRI (subsampled)
Range, Doppler 40ms PRI
Range, Angle 40ms PRI
Range, Angle, Doppler 40ms PRI
Data Size / Class
(25, 12, 64, 600)
(25, 12, 64, 600)
(25, 16, 64, 600)
(25, 16, 64, 600)
Efficiency
96.2% / 12ms
98.8% / 12.2ms
98.8% / 13ms
99.7% / 13ms
Computational time = preprocessing time + classification time
Conclusions:
Range & doppler analysis yields the most efficient classification

## Slide 24
Range FFT 40ms
Range FFT 1 Channel 40ms
Range Doppler
Range FFT
Range Doppler 1 Channel
Range, Angle, Doppler, 40ms
Range Doppler Filtered 1 Channel

## Slide 25: Dynamic Gesture Classification Results
 | Preprocessing Technique | Data Size / Class | Accuracy | Computation Time | Efficiency Score
3-Tx / 4-Rx | Range FFT | (25, 12, 512, 600) | 98.8% | 28 ms | 10.95
 | Range-Doppler FFT | (25, 12, 512, 600) | 99.2% | 28 ms | 10.99
 | Range-Doppler FFT Filtered | (25, 12, 64, 600) | 98.2% | 12 ms | 18.26
 | Range-Angle FFT | (25, 16, 512, 600) | 99% | 32 ms | 9.81
 | Range-Angle-Doppler FFT Filtered | (25, 16, 64, 600) | 99.2% | 19 ms | 14.36
 | Range-Doppler STFT Filtered | (25, 12, 13, 64, 600) | 97.5% | 35 ms | 8.90
 | Range-Angle-Doppler STFT Filtered | (25, 16, 13, 64, 600) | 98.8% | 38 ms | 8.30
 | Range FFT (8x downsampled) | (25, 12, 64, 600) | 96.2% | 12 ms | 18.08
 | Range-Doppler FFT (8x downsampled) | (25, 12, 64, 600) | 98.8% | 12 ms | 18.31
 | Range-Angle FFT (8x downsampled) | (25, 16, 64, 600) | 98.8% | 13 ms | 17.62
 | Range-Angle-Doppler FFT (8x downsampled) | (25, 16, 64, 600) | 99.7% | 13 ms | 17.70
1-Tx / 1-Rx | Range FFT (1 channel) | (25, 512, 600) | 98.5% | 9 ms | 20.78
 | Range-Doppler FFT (1 channel) | (25, 512, 600) | 99.5% | 10 ms | 19.96
 | Range-Doppler FFT Filtered (1 channel) | (25, 64, 600) | 99.5% | 8.5 ms | 21.37
 | Range-Doppler STFT Filtered (1 channel) | (25, 13, 64, 600) | 99.3% | 9 ms | 20.85
 | Range FFT (1 channel, 8x downsampled) | (25, 64, 600) | 98.5% | 8.5 ms | 21.28
 | Range-Doppler (1 channel, 8x downsampled) | (25, 64, 600) | 98.5% | 8.5 ms | 21.28

## Slide 26: Interfacing with Terahertz Sensor IC

## Slide 27: Motion Detection via Phase Extraction
Software
USRP-SDR
Signal Generator
Signal Generator
273.6GHz
200kHz
480MHz
MD-IF
250kHz
479.75GHz
50kHz
LPF
100kHz
Phase Extractor
Phase
D-IF
RF-RX
RF-TX
IF
Using THz IC, temporary setup constructed to extract relative range information from phase of IF signal by:
Single peak at 50kHz

## Slide 28: Submillimeter Relative Range Estimation
Moved radar 0.5mm radially from sensor
Uncalibrated
  Observed phase difference:
  Estimated range:
Calibrated
  Observed phase difference:
  Estimated range:

## Slide 29: Conclusions and Future Work
Using scanner to capture multiple perspectives increases static pattern classification rate substantially
Determine more THz sensing problems to investigate
Ongoing and Future Work
New applications for item detection
Continued synergy among TxACE groups to obtain THz IC
  Contacted this week requesting update
Use mechanical scanner for scenario simulation
Cascaded TI EVM Radar

## Slide 30
Questions?

## Slide 31: References
  [1] S. Rao, "Introduction to mmwave Sensing: FMCW Radars", Texas Instruments.

## Slide 32: Backup Slides

## Slide 33: Dynamic Transition Gestures

## Slide 34: Dynamic Transition Gestures
Fist
Two
Palm
C
Perpendicular (perp)
Thumbs Up (tu)
Fist
Fist
Fist
Fist
Gesture 30-50cm from radar
Torso kept away from gesture
Captures all taken consecutively
50 captures/gesture

## Slide 35: Dynamic Transition Results
2 Datasets
  Fast (5ms PRI)
  Slow (15ms PRI)
Preprocessing
  Range Angle
  Range Doppler
  Range, Angle, and Doppler
 | Slow Dataset | Fast Dataset
Range | 58% | 74%
Range Angle | 66% | 74%
Range Doppler | 72% | 78%
RAD | 72% | 86%
Fist-Tu Range vs Time
Fist-Tu Range vs Angle
Fist-C Angle vs Velocity
Conclusion: Need to leverage doppler information better

## Slide 36: Appendix of Terms
FOV: Field of View
MIMO: Multiple Input Multiple Output
FFT: Fast Fourier Transform
TDM: Time Division Multiplexing
PRI: Pulse Repetition Interval

## Slide 37: Fast SAR Imaging for Static Gestures

## Slide 38: Mechanical Imaging Scanner
2D linear mechanical scanning allows for high resolution synthetic aperture imaging

## Slide 39: MIMO Signal Model
Monostatic signal:
After some approximations:
MIMO-SAR virtual element:
Phase correction factor:

## Slide 40: Initial Results – PSF Simulation
200mm x 200mm synthetic array
8 virtual channels in vertical axis
Virtual channels allow for fewer scans

## Slide 41: Initial Results – Without Phase Correction

## Slide 42: Initial Results – With Phase Correction

## Slide 43: Hand Simulation

## Slide 44: Gun Scan – Without Thresholding

## Slide 45: Gun Scan – With Thresholding

## Slide 46: Foil Hand Scan

## Slide 47: Foil Hand Scan

## Slide 48: Human Hand Scan

## Slide 49: Human Hand Scan – With Thresholding
Bare hand has small RCS!!
Low SNR explains difficulty in accurately classifying static gestures

## Slide 50: Human Hand Scan BEST – With Thresholding

## Slide 51: Static Experiment
Can we train our model on sterile data (foil hand) and accurately classify human hand data?
6 static classes
Training: 5 human hand classes, 1 foil hand (palm) class
Results:
Control (all human data): 67.8% accuracy classifying human palms
Result (foil palm): 99% accuracy classifying human palms
Hypothesis: train with “sterile” data for improved performance and accentuated differences between classes

## Slide 52: Interfacing with Terahertz Sensor IC

## Slide 53: Motion Detection via Phase Extraction
Signal generators modulate carrier with pulse train
Software
USRP
Signal Generator
Signal Generator
273.6GHz
200kHz
480MHz
MD-IF
250kHz
479.75GHz
50kHz
LPF
100kHz
Phase Extractor
Phase
D-IF
RF-RX
RF-TX
IF

## Slide 54: Motion Detection via Phase Extraction
Received RF signal demodulated with
Phase term and pulse width contain range information
Centered at 480MHz with
harmonics 1MHz apart

## Slide 55: Motion Detection via Phase Extraction
USRP I-Q Demodulation: D-IF
Software Demodulation in MATLAB: MD-IF
Phase Extraction and Range Estimation
Single peak at 50kHz

## Slide 56: Relative Range Estimation
Moved radar 0.5mm radially from sensor
Uncalibrated
  Observed phase difference:
  Estimated range:
Calibrated
  Observed phase difference:
  Estimated range:

## Slide 57: New Applications: Conveyor Belt Scenarios using Scanner
Simple Hidden Item Detection
Hidden Item Counting
Medication Packaging
Future Applications

## Slide 58: Scenario: Hidden Item Detection
Box moves along conveyor belt at constant speed
Radar gets multiple perspectives of the box as it moves
(25, 8, 200)
Simple Case:
Is there an item in the box?
Is the box empty?
Vertically Aligned Array (8 ch)
?

## Slide 59: Mechanical Imaging Scanner
2D linear mechanical scanner
Vertically Aligned Array (8 ch)
?

## Slide 60: Using the Scanner
To simulate the conveyor belt:
Box held stationary
Scan the radar 200mm at 100mm/s capturing every 1mm
Feed range FFT into CNN for two class detection
1000 samples/class
Results:
1mm sampling: 100%
10mm subsampling: 100%
25mm subsampling 100%
-> Visually obvious in the range FFT

## Slide 61: Hidden Item Counting

## Slide 62: Scenario: Hidden Item Counting
Box moves along conveyor belt at constant speed
Radar gets multiple perspectives of the box as it moves
Four Cases:
No Items
1 Metal Item
2 Metal Items (10cm apart)
3 Metal Items

## Slide 63: Using the Scanner
To simulate the conveyor belt:
100 samples/class
Scan the radar 200mm at 100mm/s capturing every 1mm
Feed range FFT into CNN for four class detection
Results:
1mm sampling: 100%
10mm subsampling: 100%
25mm subsampling 100%
-> Still visually observable in the range FFT

## Slide 64: Medication Packaging

## Slide 65: Scenario: Medication Packing
Box moves along conveyor belt at constant speed
Radar gets multiple perspectives of the box as it moves
Insert always facing radar
Box contains:
Pills in bottle and insert
Pills in bottle and no insert

## Slide 66: Using the Scanner
To simulate the conveyor belt:
600 samples/class (every 10 box is at different location)
Scan the radar 200mm at 100mm/s capturing every 1mm
Feed range FFT into CNN for four class detection
Results:
1mm sampling: 100%
10mm subsampling: 100%
25mm subsampling 99.7%
-> Very minor change in the range FFT (but detectable by CNN)

## Slide 67: Future Applications

## Slide 68: Automotive Scene Classification
Radar continuously capturing images from a moving vehicle
Estimate the range of targets in various environments
Target classification: human, stationary object, another vehicle (stationary or moving)
Initial Steps:
Capture dynamic motions with scanner
Classify human movements
Image Courtesy of TI