## Slide 1: Terahertz Imaging Toolbox with Interactive User Interface
Motivation
5. Summary
Acknowledgments
Josiah W. Smith1, Murat Torlak1
1The University of Texas at Dallas, 800 W Campbell Rd Richardson, TX 75080
As terahertz systems become increasingly viable, there is a need for efficient system prototyping, algorithm development, and ML dataset generation
1. Background
Future Work
2. MATLAB Interface
3. THz Simulation Steps
4. Machine Learning Dataset Generation
Publication
Training neural processors requires access to large, meaningful datasets
Supervised learning  features and corresponding labels
Solution: our simulation platform can efficiently generate large datasets for ML training
Previous work on THz simulation platforms has been limited to far-field simulation or computationally-expensive antenna simulation.
We present a new MATLAB-based approach to THz imaging simulation enabling rapid THz system prototyping, imaging algorithm development, and machine learning model training.
This work is supported by Texas Instruments through Foundational Technology Research Centre (FTRC).
Full control over transmitted waveform
Create antenna gain pattern and MIMO array
Set scanning scenario
Create target scene to image
  Point reflectors at specified locations
  Import 2-D images
  Import 3-D STL files
  Generate randomly placed points (dataset generation)
Reconstruct the image
  Use built-in algorithms
  Develop, test custom imaging algorithms
  Rapidly prototype THz imaging systems
(1) - Waveform
(3) - SAR Scan
(4) - Target
(5) - Image
(2) - Antenna
Features: distorted reconstructed images
Labels: ideal input reflectivity intensity maps
Neural Processor (CNN-based)
Real 77GHz Results
Reduced noise floor ~15dB
Our simulation interface enables:
Rapid prototyping of THz imaging systems
Simplified imaging algorithm development
Machine learning applications built on THz imaging by efficient dataset generation of high-fidelity data
Extend simulation platform capabilities
  Target material properties
  Varying propagation media (through-the-wall)
  Multipath effects
Develop neural processors for improved imaging
  Hybrid signal processing + ML
  Exceeds theoretical spatial/spectral resolution
[1] J. W. Smith and M. Torlak, “Terahertz Imaging Toolbox with Interactive User Interface,” Submitted in IEEE Open Journal on Antennas and Propagation
Input
Output